提示：系统监测到该条供求信息的发布时间过于久远，可能已经无效！

# AMS200赛高计量泵

| 商机面向地区： | 上海 嘉定区 |
| --- | --- |
| 供求信息分类： | 电子/仪表 仪器/仪表 |
| 发布日期： | 2018年4月21日 |
| 销售信息： | 供应 AMS200赛高计量泵 |

AMS200赛高计量泵，AMS201计量泵，SEKO计量泵 KOMPACT系列电磁隔膜式赛高泵AMS200 Kompact系列是基于微处理器控制的电磁驱动赛高泵，具有操作简单，运行稳定的特点。 规格参数： 流量：5L/H 时压力 8BAR 3L/H时压力10BAR 连接管尺寸（MM）：4*6（内径*外径） 冲程/分钟：160 泵壳材质：PP 泵头材质：PVDF 防护等级：IP65 带排气阀 进出口阀：PVDF 阀球材质：陶瓷 隔膜：PTFE（隔膜的使用寿命可达5年） AMS200 电磁赛高泵 通过控制面板上的调节旋钮可对流量进行手动调节，还带有电源指示。 Constant flow rate manually adjustable by control dial on the front panel,Power-ON led indicator. AML200电磁隔膜赛高泵 通过控制面板上的调节旋钮可对流量进行手动调节，两种流量范围可选：0-20%和0-100% 带液位探头接口，可直接连接液位开关控制赛高泵的启动和停止。 iConstant flow rate manually adjustable by control dial on the front panel, two flow rate range: 0÷20% with switch in P position, 0÷100% with switch in C position, Power-ON led indicator and level control input. AMM200自控型电磁赛高泵 可手动调节，也可以比例调节。可根据外部模拟信号（4-20毫安）来调节流量比例，带有电源指示灯和液位探头接口，可直接连接液位探头控制赛高泵启动或停止。 Constant flow rate manually adjustable, proportional flow rate according to an external analogue signal (4÷20 mA), Power-ON led indicator and level control input. The two different modes are: Constant (switch in C position) The pump constantly doses the rate selected with the potentiometer. Proportional (switch in P position) The pump doses proportionally to the analogue input signal (4÷20 mA). AMC200自控型隔膜赛高泵 比例调节，可根据数字信号（比如水表发出的脉冲信号）来调节流量的比例，带有电源指示和液位探头接口，可直接连接液位探头控制赛高泵启动或停止。 Constant flow rate manually adjustable, proportional flow rate according to a digital input signal (from water meter), Power-ON led indicator and level control input. The two different modes are: Constant (switch in C position) The pump constantly doses the rate selected with the potentiometer. Proportional (switch in P position) The pump doses proportionally to the digital input signal (Divisi主要产品有：台湾上泰SUNTEX，意大利B&C，德国WTW，美国JENCO，特色产品有：轮椅秤，轮椅称，电子轮椅秤，医用轮椅秤，透析电子秤，轮椅电子秤，欢迎联系：http://www.shslgs.com/ 上海升隆电子科技有限公司供应PH酸度计,电导率等水质检测仪,代理销售台湾上泰仪器,瑞士梅特勒PH计。 on mode 4 : 1). Maximum input frequency: 80Hz.

# 上海升隆电子科技有限公司

| 企业地址： |  | 企业邮编： |  |
| --- | --- | --- | --- |
| 联系电话： |  | 所属行业： | 通信/仪表 |
| 公司传真： |  | 公司所在地： | 上海 嘉定区 |
| 公司网站： |  | 企业类型： | 中外合资 |
| 电子邮件： |  | 联系人： |  |
| 企业全称： | 上海升隆电子科技有限公司 |  |  |

未填写

上海升隆电子科技有限公司 发布的其它供求信息和贸易商机：

| 供应 >工业设备'>DC-5300上泰，上泰DC-5310 | 2018年4月21日 |
| --- | --- |
| 供应 >工业设备'>上泰DC-5310RS溶解氧 | 2018年4月21日 |
| 供应 >量器量具'>SEKO赛高计量泵，AKS600计量泵 | 2018年4月21日 |
| 供应 >生产设备'>SEKO赛高计量泵，AKS赛高泵 | 2017年12月16日 |
| 供应 >工业设备'>AKS500NHP1800赛高计量泵 | 2018年4月21日 |
| 供应 >技术合作'>SEKO赛高计量泵，西科计量泵 | 2018年4月21日 |
| 供应 >化工设备仪器'>AMC200赛高计量泵 | 2018年4月21日 |
| 供应 >水处理'>AMM200赛高计量泵 | 2018年4月21日 |
| 供应 >工业设备'>AML201赛高计量泵 | 2018年4月21日 |

本文档来源于：商业机器人（www.bizrobot.com），所有内容由用户发布，与本站无关