提示：系统监测到该条供求信息的发布时间过于久远，可能已经无效！

# 特威DeVilbissAGMDpro喷枪

| 商机面向地区： | 广东 深圳市 |
| --- | --- |
| 供求信息分类： | 工业用品 气动工具 |
| 发布日期： | 2019年4月19日 |
| 商机联系人： | 孙生 |
| 供求电话： | 13823127806 |
| 电子邮件： | 47586327@qq.com |
| 销售信息： | 供应 特威DeVilbissAGMDpro喷枪 |

Our engineers have taken acknowledged leading atomization technology and enhanced the market leading AGMD Automatic gun to produce the “AGMD PRO”. Now incorporating LVMP Compliant SPRAY performance with results to match and exceed that of the traditional air caps used today. This new platform of Automatic gun technology has the ability to improve Transfer Efficiency while also providing reduced air consumption. Improved maintenance and serviceability comes as standard from the AGMD PRO which is vital for the high demand finishing industries. A choice of three new high performance air caps are available ensuring the AGMD PRO gun is the ultimate choice for industrial finish quality. The new design AGMD PRO features a simple quick detach gun head which provides reduced production downtime allowing servicing exchange for maintenance in seconds. The improved internal fluid passages facilitate efficient color change and flushing cycles required by Class A finishes. The AGMD PRO gun can be configured for standard machine mount applications or upon adapters and hose bundles suitable for most common painting robots. DeVilbiss LVMP Compliant Atomization Technology “Pro” high performance front end technology with removable/replaceable baffle and air cap retaining threads New radial clamping device with quick release cam operation from either side of gun – compact and convenient Fast cylinder cycle at lower air pressures Same “Tool Center Point” as original AGMD model Certified air caps with indexing facility Plastic tip needle on St/St seat for increased life Suitable for waterborn and solvent base coatings DEVILBISS AGMD PRO Automatic spray gun The DeVilbiss AGMD Pro Automatic spray gun delivers optimal atomization quality and the best performance in its class

# 深圳市立扬科技有限公司

| 企业地址： |  | 企业邮编： |  |
| --- | --- | --- | --- |
| 联系电话： |  | 所属行业： | 机械设备 |
| 公司传真： |  | 公司所在地： | 广东 深圳市 |
| 公司网站： |  | 企业类型： | 国有企业 |
| 电子邮件： | 47586327@qq.com | 联系人： |  |
| 企业全称： | 深圳市立扬科技有限公司 |  |  |

未填写

深圳市立扬科技有限公司 发布的其它供求信息和贸易商机：

| 供应 >气动工具'>特威DeVilbit-agb360喷枪 | 2019年4月19日 |
| --- | --- |
| 供应 >气动工具'>特威GTIProlite喷枪 | 2019年4月19日 |
| 供应 >气动工具'>特威DeVilbissfun-cy喷枪 | 2019年4月19日 |
| 供应 >气动工具'>特威Cobra1Cobra2喷枪 | 2019年4月19日 |
| 供应 >气动工具'>特威DeVilbissAGX喷枪 | 2019年4月19日 |
| 供应 >气动工具'>特威DeVilbissAGXV喷枪 | 2019年4月19日 |
| 供应 >气动工具'>特威DeVilbissAG-362喷枪 | 2019年4月19日 |
| 供应 >气动工具'>特威DeVilbissAG-361喷枪 | 2019年4月19日 |

本文档来源于：商业机器人（www.bizrobot.com），所有内容由用户发布，与本站无关